## Slide 1
Adaptive sinusoidal spectral matching
for out-of-plane masonry walls
Four Route 2 methods tested from the common Strategy F Run 21 state
Progress meeting, Hanze SAFEGo US-1, 5 October 2026
Notes: This update focuses on the four Route 2 carrier and target combinations. Each sequence starts from the same Strategy F Run 21 save and carries the damage state forward through FR76 Runs 22–25.

## Slide 2
1
Four Route 2 methods
Two target rules crossed with two Wave B carrier periods
Method 1
B target: scale × Sd(Teff)
B carrier: Teff = 0.241 s
Wave A · T1 = 0.112 s
Wave B · carrier shown above
Method 2
B target: scale × Sd(Teff)
B carrier: record Tp = 0.260 s
Wave A · T1 = 0.112 s
Wave B · carrier shown above
Method 3
B target: (T*, d*) by intensity
B carrier: T* = 0.134 s
Wave A · T1 = 0.112 s
Wave B · carrier shown above
Method 4
B target: (T*, d*) by intensity
B carrier: record Tp = 0.260 s
Wave A · T1 = 0.112 s
Wave B · carrier shown above
Methods 3–4 use precomputed capacity-proxy targets that vary with intensity. The schedule is independent of the preceding 3DEC response.
Notes: Wave A is common to all four methods and targets scale × Sd(T1), where T1 is about 0.1119 s. Methods 1 and 2 use fixed target points at T1 and Teff, with Teff about 0.2414 s. Methods 3 and 4 use the precomputed capacity-proxy target d* and T* for each intensity. Method 1 carries Wave B at Teff; Method 2 uses the FR76 predominant period Tp = 0.260 s; Method 3 carries Wave B at T*; Method 4 uses Tp. The adaptive schedule is precomputed and independent of the preceding 3DEC response.

## Slide 3
2
Peak response and spectral calibration
Runs 22–24 compare with US-1 Test 9; Run 25 has no matching specimen test
17.1%
Method 2 mean OOP error
9.3%
Method 1 mean base-shear peak error
All 16 spectral fits missed the 2% convergence tolerance. Treat these response rankings as provisional.
Notes: Metrics use the three experimental comparisons available for US-1 Test 9, Runs 22–24. Method 2 has the lowest mean absolute percentage error in peak relative OOP displacement at 17.1%. Method 1 has the lowest mean absolute percentage error in peak base shear at 9.3%. Run 25 is shown for the model sequence only because no US-1 Test 9 experiment exists for that run. The four methods used the common Strategy F Run 21 starting state. All 16 signal fits report fit_converged=False at the 2% tolerance, so the method ranking is preliminary.

## Slide 4
3
Base shear versus OOP displacement: Method 1
Like-for-like loops from baseshear_exp_from_model.py
US-1 Test 9 is the primary experimental comparator. US-2 Test 12 and the support series remain visible in the source figure.
Base-shear mass basis
Tributary masses use ρ = 1,619 kg/m³; the ×2.317348 test factor is applied to both model and experiment.
Mean base-shear peak error
9.3%
Notes: Method 1 uses the per-method plot generated from the project copy of Claude outputs/baseshear_exp_from_model.py. The script sums tributary masses at sensors 15–17 using ρ = 1,619 kg/m³ and applies MASS_SCALE = 2.317348 to both the model and experimental sides. The source figure also retains US-2 Test 12 and the support reaction traces. The reported mean base-shear peak error is the mean absolute percentage error over the three available US-1 Test 9 comparisons, Runs 22–24.

## Slide 5
4
Base shear versus OOP displacement: Method 2
Like-for-like loops from baseshear_exp_from_model.py
US-1 Test 9 is the primary experimental comparator. US-2 Test 12 and the support series remain visible in the source figure.
Base-shear mass basis
Tributary masses use ρ = 1,619 kg/m³; the ×2.317348 test factor is applied to both model and experiment.
Mean base-shear peak error
13.3%
Notes: Method 2 uses the per-method plot generated from the project copy of Claude outputs/baseshear_exp_from_model.py. The script sums tributary masses at sensors 15–17 using ρ = 1,619 kg/m³ and applies MASS_SCALE = 2.317348 to both the model and experimental sides. The source figure also retains US-2 Test 12 and the support reaction traces. The reported mean base-shear peak error is the mean absolute percentage error over the three available US-1 Test 9 comparisons, Runs 22–24.

## Slide 6
5
Base shear versus OOP displacement: Method 3
Like-for-like loops from baseshear_exp_from_model.py
US-1 Test 9 is the primary experimental comparator. US-2 Test 12 and the support series remain visible in the source figure.
Base-shear mass basis
Tributary masses use ρ = 1,619 kg/m³; the ×2.317348 test factor is applied to both model and experiment.
Mean base-shear peak error
14.7%
Notes: Method 3 uses the per-method plot generated from the project copy of Claude outputs/baseshear_exp_from_model.py. The script sums tributary masses at sensors 15–17 using ρ = 1,619 kg/m³ and applies MASS_SCALE = 2.317348 to both the model and experimental sides. The source figure also retains US-2 Test 12 and the support reaction traces. The reported mean base-shear peak error is the mean absolute percentage error over the three available US-1 Test 9 comparisons, Runs 22–24.

## Slide 7
6
Base shear versus OOP displacement: Method 4
Like-for-like loops from baseshear_exp_from_model.py
US-1 Test 9 is the primary experimental comparator. US-2 Test 12 and the support series remain visible in the source figure.
Base-shear mass basis
Tributary masses use ρ = 1,619 kg/m³; the ×2.317348 test factor is applied to both model and experiment.
Mean base-shear peak error
17.1%
Notes: Method 4 uses the per-method plot generated from the project copy of Claude outputs/baseshear_exp_from_model.py. The script sums tributary masses at sensors 15–17 using ρ = 1,619 kg/m³ and applies MASS_SCALE = 2.317348 to both the model and experimental sides. The source figure also retains US-2 Test 12 and the support reaction traces. The reported mean base-shear peak error is the mean absolute percentage error over the three available US-1 Test 9 comparisons, Runs 22–24.

## Slide 8
7
Experimental tiltmeter residuals
Settled Y-axis readings after each run; no experimental Run 25 reading is available
Chart: FR76 sequence run
| 21 | 22 | 23 | 24
US-1 Test 9 | 2.756 | 2.529 | 2.3965 | 6.035
+3.279°
Run 24 change from the Run 21 baseline
Within-shaking inclinometer peaks clip near ±25.75°, so this chart uses settled residuals only.
A model comparison needs the angle at the instrument location. The local chord-angle proxy is excluded.
Notes: Experimental points are read from Claude outputs/exp_Test9_incl_tilt.csv, column resid_tilt_y_deg: Run 21 = 2.756°, Run 22 = 2.529°, Run 23 = 2.3965°, and Run 24 = 6.035°. Run 24 is +3.279° relative to Run 21. The within-shaking inclinometers clip near ±25.75°; this figure therefore uses settled residuals. No matched model instrument-point tilt series is presented. The current local chord-angle proxy is deliberately excluded from this experimental comparison.

## Slide 9
8
What these runs support
Four methods, one common starting state, and three matched US-1 runs
17.1%
Method 2
Lowest mean OOP
displacement error
9.3%
Method 1
Lowest mean base-shear
peak error
16 / 16
All methods
Spectral fits outside
2% tolerance
Method 2 leads on displacement, while Method 1 leads on base-shear peak. No single method leads on both.
Next: improve the joint two-wave spectral fit, then compare model tilt at the instrument location.
Runs 22–24 have US-1 comparisons. Run 25 is model-only. All methods start from Strategy F Run 21.
Notes: The mean error metrics compare Methods 1–4 against US-1 Test 9 for Runs 22–24. Method 2 gives the lowest mean absolute OOP displacement error at 17.1%; Method 1 gives the lowest mean absolute base-shear peak error at 9.3%. These four runs do not identify one overall winner. All spectral calibration fits missed the 2% convergence tolerance, so first improve the joint two-wave fit. Then generate a model tilt measure at the actual inclinometer location and compare settled residuals before selecting a method.