## Slide 1
Adaptive sinusoidal spectral matching
for out-of-plane masonry walls
Four Route 2 methods tested from the common Strategy F Run 21 state
Progress meeting, Hanze SAFEGo US-1 + US-2, 5 October 2026
Notes: This update focuses on the four Route 2 carrier and target combinations. Each sequence starts from the same Strategy F Run 21 save and carries the damage state forward through FR76 Runs 22–25.

## Slide 2
1
Four Route 2 methods
Two target rules crossed with two Wave B carrier periods
Method 1
B target: scale × Sd(Teff)
B carrier: Teff = 0.241 s
Wave A · T1 = 0.112 s
Wave B · carrier shown above
Method 2
B target: scale × Sd(Teff)
B carrier: record Tp = 0.260 s
Wave A · T1 = 0.112 s
Wave B · carrier shown above
Method 3
B target: (T*, d*) by intensity
B carrier: T* = 0.134 s
Wave A · T1 = 0.112 s
Wave B · carrier shown above
Method 4
B target: (T*, d*) by intensity
B carrier: record Tp = 0.260 s
Wave A · T1 = 0.112 s
Wave B · carrier shown above
Target = desired spectral displacement at an oscillator period. Carrier = input sine period. The fit adjusts wave velocities with carrier periods fixed; Methods 3–4 use precomputed targets.
Notes: Wave A is common to all four methods and targets scale × Sd(T1), where T1 is about 0.1119 s. Methods 1 and 2 use fixed target points at T1 and Teff, with Teff about 0.2414 s. Methods 3 and 4 use the precomputed capacity-proxy target d* and T* for each intensity. Method 1 carries Wave B at Teff; Method 2 uses the FR76 predominant period Tp = 0.260 s; Method 3 carries Wave B at T*; Method 4 uses Tp. The amplitude fit changes the two input velocity amplitudes while the carrier periods remain prescribed. The adaptive schedule is precomputed and independent of the preceding 3DEC response.

## Slide 3
2
Reading targets at fixed periods
T1 and Teff come from the wall idealisation; each run supplies a scaled record spectrum
Chart: Scaled spectral displacement Sd (mm)
Guides: T1 = 0.112 s (dark) · Teff = 0.241 s (terracotta)
Curves: HU12 (blue, 21 runs) · EC40 (green, 4 runs) · FR76 (terracotta, 4 runs)
Wave A target = scale × Sd(T1) · Method 1 Wave B target = scale × Sd(Teff)
Notes: All 25 lines are the 5%-damped displacement spectra for the run's ground-motion record multiplied by that run's protocol scale. T1 = 0.111887 s and Teff = 0.241382 s are the fixed periods from the wall's bilinear pushover idealisation and are reused for every run. For each run, the ordinate read at T1 sets the Wave A spectral-displacement target, and the ordinate read at Teff sets Method 1's Wave B target. The chart zooms the period axis to 0–0.35 s to make both fixed target periods legible. The lines are grouped by record; repeated curves have different protocol scales.

## Slide 4
3
Method 3 target for Run 22
A stable fixed point between the scaled FR76 spectrum and the cracked pushover backbone
d* = 1.00 × Sd,FR76(Tsec(d*))
Tsec(d) = 2π √[ meff / (Fcracked(d) / d) ]
TRIAL DISPLACEMENT
3.423 mm
Run 22 · FR76 × scale 1.00
PUSHOVER SECANT
12.360 kN
Fcracked at d* · ksec = F/d = 3.611 kN/mm
READ THE SPECTRUM
0.133704 s
Tsec → Sd,FR76 = 3.423 mm
meff = 1,635 kg → Tsec = 2π√(1,635 / 3.611×10⁶) = 0.133704 s
At that period, FR76 gives Sd = 3.423 mm. Demand equals the trial displacement, so this is d*.
The cracked backbone follows the precomputed target schedule after an earlier target crossed dy; Run 21's measured response is not used.
Notes: The value d*=3.423165 mm is read from Claude outputs/casm_step1_targets.csv for Run 22, FR76 at scale 1.00. The calculation uses the actual pushover force-displacement backbone and the 5%-damped FR76 spectrum. At d=3.423165 mm the cracked backbone gives F=12.360003 kN, hence F/d=3.610694 kN/mm. With m_eff=1635 kg, the secant-period calculation gives T*=0.133703694 s. Linear interpolation of the FR76 spectrum at that period gives Sd=3.423165 mm, so scale × Sd(Tsec(d)) equals d. The script numerically scans and interpolates the first stable crossing. The target schedule's cracked-backbone state is property-based damage memory: it switches after an earlier scheduled d* crossed dy; it does not read the measured Run 21 or Run 22 3DEC response. Method 3 uses this T* as its Wave B carrier before snapping to the 0.135 s time-grid period.

## Slide 5
4
Run 22 input velocity
Actual FR76 × 1.00 velocity tables imported into 3DEC · Wave A is common to all methods
Chart: Applied table velocity (m/s)
Method 3 · T_B = 0.135 s | 0 | 0.00227 | 0.0043562 | 0.0060894 | 0.0073293 | 0.0079754 | 0.0079754 | 0.0073293 | 0.0060894 | 0.0043562 | 0.00227 | 9.8675e-19 | -0.00227 | -0.0043562 | -0.0060894 | -0.0073293 | -0.0079754 | -0.0079754 | -0.0073293 | -0.0060894 | -0.0043562 | -0.00227 | -1.9735e-18 | 0.013019 | 0.025336 | 0.036287 | 0.045282 | 0.051835 | 0.055595 | 0.056357 | 0.054081 | 0.048889 | 0.041062 | 0.031021 | 0.019308 | 0.0065537 | -0.0065537 | -0.019308 | -0.031021 | -0.041062 | -0.048889 | -0.054081 | -0.056357 | -0.055595 | -0.051835 | -0.045282 | -0.036287 | -0.025336 | -0.013019 | -1.3827e-17
Wave A carrier = 0.110 s in every method. The fitting routine changes the Wave A/B velocity amplitudes; the selected carrier periods stay fixed.
Notes: Each series is read from the corresponding Run22_FR76_s1p00_*_vel.txt table saved in route2_four_methods and imported by the 3DEC Itasca Python script. These are the applied boundary/table velocities at the native 0.005 s sample interval, not wall response velocities. The common Wave A carrier is 0.110 s on the input grid. Wave B grid periods are 0.240 s, 0.260 s, 0.135 s, and 0.260 s for Methods 1–4. The carrier periods are set by each method; the joint spectral fit adjusts the component velocities.

## Slide 6
5
Peak response and spectral calibration
Runs 22–24 compare with US-1 Test 9; Run 25 has no matching specimen test
17.1%
Method 2 mean OOP error
9.3%
Method 1 mean base-shear peak error
All 16 spectral fits missed the 2% convergence tolerance. Treat these response rankings as provisional.
Notes: Metrics use the three experimental comparisons available for US-1 Test 9, Runs 22–24. Method 2 has the lowest mean absolute percentage error in peak relative OOP displacement at 17.1%. Method 1 has the lowest mean absolute percentage error in peak base shear at 9.3%. Run 25 is shown for the model sequence only because no US-1 Test 9 experiment exists for that run. The four methods used the common Strategy F Run 21 starting state. All 16 signal fits report fit_converged=False at the 2% tolerance, so the method ranking is preliminary.

## Slide 7
6
Peak-response comparison: Method 2 highlighted
Methods 1, 3 and 4 are muted; the experimental series remains visible
Method 2 has the lowest mean peak OOP error (17.1%); Method 1 still has the lowest base-shear error (9.3%).
All 16 spectral fits missed the 2% convergence tolerance; treat these rankings as provisional.
Notes: This is a visual focus transition from the preceding all-method comparison. Methods 1, 3 and 4 use one pale grey with partial transparency; Method 2 retains its orange emphasis, and the US-1 experiment remains black. The underlying data are unchanged. Method 2 has the lowest mean absolute peak relative OOP displacement error at 17.1%, while Method 1 has the lowest mean absolute peak base-shear error at 9.3%. All 16 spectral fits missed the 2% convergence tolerance, so these rankings remain preliminary.

## Slide 8
7
Two base-shear measures
cstav is a model support reaction; the test reports an inertia-derived estimate
DIRECT 3DEC OUTPUT
cstav
V_cstav(t) = sign × [cstav(t) − cstav(0)]
What it measures
The net reaction from the model’s base and joist supports, read directly from the 3DEC history.
Kept as a grey reference trace. It is not the quantity reported by the experimental processing formula.
TEST-COMPATIBLE INERTIA ESTIMATE
V_eq = sign × (λ / 1000) Σ m_j a_j,abs
kN · sign aligned and each run zeroed at its start
Acc 17 · z = 2.06 m
m17 = 404.13 kg
Acc 16 · z = 1.26 m
m16 = 320.66 kg
Acc 15 · z = 0.60 m
m15 = 408.52 kg
3DEC MODEL
Differentiate absolute sensor velocities; resample at 0.5 ms and low-pass at 50 Hz.
EXPERIMENT
Use table acceleration plus the wall accelerometers to reconstruct absolute acceleration.
LIKE-FOR-LIKE COMPARISON
The same Σm·a definition is used for the experimental data and reconstructed from the model’s sensor histories. Base-shear errors on the next slides use this estimate; cstav stays as context.
Mass basis: ρ = 1,619 kg/m³ gives the tributary masses above. λ = 2.317348 reproduces the factor in the processed tests and is applied to both sides; its origin is not confirmed.
Loops use relative OOP displacement at z = 2.06 m on the horizontal axis.
Notes: cstav is the direct model support reaction from the base and joist supports; the existing source plots it as a grey context trace. The experimental base shear is derived from accelerometer inertia (Moshfeghi et al. 2024, Eq. 2), not cstav. It uses the three sensor-point absolute accelerations at z=0.60, 1.26, and 2.06 m, weighted by tributary masses 408.52, 320.66, and 404.13 kg. The model side reconstructs those absolute accelerations by differentiating absolute out-of-plane velocities, resampling at 0.5 ms, and applying a 50 Hz low-pass filter. The processed test formula combines table acceleration and wall accelerometer channels to get absolute acceleration. The factor lambda=2.317348 is applied to both sides to reproduce the factor embedded in the processed tests; its origin is unknown and remains a question. Curves are start-zeroed, sign-aligned, and plotted against relative OOP displacement at 2.06 m. The reported model-to-test peak base-shear errors use the experimental-derived sum(m*a) quantity, not cstav.

## Slide 9
8
Base shear versus OOP displacement: Method 1
Like-for-like loops from baseshear_exp_from_model.py
US-1 Test 9 is the primary experimental comparator. US-2 Test 12 and the support series remain visible in the source figure.
Base-shear mass basis
Tributary masses use ρ = 1,619 kg/m³; the ×2.317348 test factor is applied to both model and experiment.
US-1 mean base-shear peak error
9.3%
Notes: Method 1 uses the per-method plot generated from the project copy of Claude outputs/baseshear_exp_from_model.py. The script sums tributary masses at sensors 15–17 using ρ = 1,619 kg/m³ and applies MASS_SCALE = 2.317348 to both the model and experimental sides. The source figure retains both US-1 Test 9 and US-2 Test 12, plus the support reaction traces. The displayed mean base-shear peak error is specific to US-1 Test 9, Runs 22–24; a separate slide scores US-2 over Runs 22–25.

## Slide 10
9
Base shear versus OOP displacement: Method 2
Like-for-like loops from baseshear_exp_from_model.py
US-1 Test 9 is the primary experimental comparator. US-2 Test 12 and the support series remain visible in the source figure.
Base-shear mass basis
Tributary masses use ρ = 1,619 kg/m³; the ×2.317348 test factor is applied to both model and experiment.
US-1 mean base-shear peak error
13.3%
Notes: Method 2 uses the per-method plot generated from the project copy of Claude outputs/baseshear_exp_from_model.py. The script sums tributary masses at sensors 15–17 using ρ = 1,619 kg/m³ and applies MASS_SCALE = 2.317348 to both the model and experimental sides. The source figure retains both US-1 Test 9 and US-2 Test 12, plus the support reaction traces. The displayed mean base-shear peak error is specific to US-1 Test 9, Runs 22–24; a separate slide scores US-2 over Runs 22–25.

## Slide 11
10
Base shear versus OOP displacement: Method 3
Like-for-like loops from baseshear_exp_from_model.py
US-1 Test 9 is the primary experimental comparator. US-2 Test 12 and the support series remain visible in the source figure.
Base-shear mass basis
Tributary masses use ρ = 1,619 kg/m³; the ×2.317348 test factor is applied to both model and experiment.
US-1 mean base-shear peak error
14.7%
Notes: Method 3 uses the per-method plot generated from the project copy of Claude outputs/baseshear_exp_from_model.py. The script sums tributary masses at sensors 15–17 using ρ = 1,619 kg/m³ and applies MASS_SCALE = 2.317348 to both the model and experimental sides. The source figure retains both US-1 Test 9 and US-2 Test 12, plus the support reaction traces. The displayed mean base-shear peak error is specific to US-1 Test 9, Runs 22–24; a separate slide scores US-2 over Runs 22–25.

## Slide 12
11
Base shear versus OOP displacement: Method 4
Like-for-like loops from baseshear_exp_from_model.py
US-1 Test 9 is the primary experimental comparator. US-2 Test 12 and the support series remain visible in the source figure.
Base-shear mass basis
Tributary masses use ρ = 1,619 kg/m³; the ×2.317348 test factor is applied to both model and experiment.
US-1 mean base-shear peak error
17.1%
Notes: Method 4 uses the per-method plot generated from the project copy of Claude outputs/baseshear_exp_from_model.py. The script sums tributary masses at sensors 15–17 using ρ = 1,619 kg/m³ and applies MASS_SCALE = 2.317348 to both the model and experimental sides. The source figure retains both US-1 Test 9 and US-2 Test 12, plus the support reaction traces. The displayed mean base-shear peak error is specific to US-1 Test 9, Runs 22–24; a separate slide scores US-2 over Runs 22–25.

## Slide 13
12
US-2 is a separate benchmark
The Test 12 displacement path stays low through Run 24, then rises sharply at Run 25
Chart: Peak relative OOP displacement (mm)
| 22 | 23 | 24 | 25
Method 1 | 3.3132 | 24.0228 | 31.823 | 34.1371
Method 2 | 2.4738 | 12.1028 | 32.7545 | 41.014
Method 3 | 3.5841 | 5.8417 | 7.4077 | 9.9228
Method 4 | 2.25 | 5.3268 | 28.2426 | 36.3054
US-1 Test 9 | 3.6473 | 13.1536 | 29.4828
US-2 Test 12 | 2.3847 | 5.2645 | 7.5808 | 31.1419
Chart: Peak experiment-equivalent base shear (kN)
| 22 | 23 | 24 | 25
Method 1 | 17.7439 | 29.0586 | 31.8247 | 36.527
Method 2 | 18.4502 | 26.5624 | 38.0256 | 32.525
Method 3 | 21.3379 | 20.0858 | 25.5861 | 22.9949
Method 4 | 20.9988 | 21.8173 | 37.98 | 39.8456
US-1 Test 9 | 20.3266 | 27.041 | 29.5
US-2 Test 12 | 21.1914 | 27.8652 | 29.9902 | 38.0722
RUN 24
3.9×
US-1: 29.48 mm · US-2: 7.58 mm
US-2 RUN 25
31.14 mm
Large excursion; US-1 has no Run 25 test.
US-2 MEAN ABSOLUTE ERROR
OOP: M3 32.9% · Shear: M1 7.7%
Four measured runs (22–25), scored separately.
The model sequences start from the US-1 Strategy F Run 21 state; Test 12 is an independent specimen check. US-1 and US-2 are not pooled.
Notes: US-2 Test 12 workbooks were post-processed with the same start-zero peak definition used for US-1: U_avg converted from metres to millimetres, and processed base_shear_kN zeroed at each run start. The four method response peaks are compared with the four Test 12 observations, Runs 22–25; these sequences all start from the common US-1 Strategy F Run 21 model state. US-2 peaks are 2.385, 5.264, 7.581, and 31.142 mm displacement, with 21.191, 27.865, 29.990, and 38.072 kN base shear. US-2 Run 24 displacement is 7.58 mm against US-1's 29.48 mm, while Test 12 then reaches 31.14 mm at Run 25. Mean absolute percentage errors over Runs 22–25: Method 3 is lowest for displacement (32.9%) and Method 1 is lowest for base shear (7.7%). Method 3's Run 25 model displacement is only 9.92 mm, so its good mean is driven by Runs 22–24 and it misses the final large excursion. The different best methods, and the abrupt Test 12 transition, show specimen-specific sensitivity rather than a universal winner.

## Slide 14
13
Experimental tiltmeter residuals
Settled sensor readings for US-1 and US-2; only US-2 has a Run 25 observation
Chart: Settled residual tilt Y (degrees)
| 21 | 22 | 23 | 24
US-1 Test 9 | 2.756 | 2.529 | 2.3965 | 6.035
US-2 Test 12 | 1.223 | 1.0225 | 0.385 | 0.944 | 2.288
US-1 +3.279°
Run 24 change from its Run 21 reading
US-2 +1.065°
Run 25 change; settled reading 2.288°
Within-shaking peaks clip near ±25.75°; this plot uses settled residual readings only.
These are instrument readings. The model's local-chord angle is excluded from this comparison.
Notes: US-1 values come from Claude outputs/exp_Test9_incl_tilt.csv: Runs 21–24 = 2.756, 2.529, 2.3965, and 6.035 degrees; Run 24 is +3.279 degrees relative to Run 21. US-2 values are recomputed from EXP_DATA/US2_Tilt_values.csv, using the logger's accelerometer activity to identify 25 events and the settled median after each event relative to the first five samples. Runs 21–25 = 1.223, 1.0225, 0.385, 0.944, and 2.288 degrees; US-2 Run 25 is +1.065 degrees relative to Run 21. The within-shaking inclinometer peaks clip near ±25.75 degrees, so settled readings are shown. This slide compares the two experimental instruments only; it does not plot the model's local-chord tilt proxy.

## Slide 15
14
What these runs support
The method ranking depends on response metric and specimen
17.1%
Method 2
Lowest US-1 mean OOP
displacement error
9.3%
Method 1
Lowest US-1 mean base-shear
peak error
16 / 16
All methods
Spectral fits outside
2% tolerance
US-2 adds a different result: Method 3 best matches its displacement average, while Method 1 best matches base shear.
Method 3 still misses the sharp US-2 Run 25 displacement jump; refine the fit and investigate this transition.
US-1 is scored over Runs 22–24; US-2 over Runs 22–25. Tests stay separate; models start from US-1 Strategy F Run 21.
Notes: The headline US-1 metrics compare Runs 22–24: Method 2 has the lowest mean absolute OOP error at 17.1%, and Method 1 the lowest mean absolute base-shear peak error at 9.3%. The separate US-2 score over Runs 22–25 gives Method 3 the lowest OOP MAPE at 32.9% and Method 1 the lowest base-shear MAPE at 7.7%. Method 3 predicts only 9.92 mm at US-2 Run 25 versus the measured 31.14 mm. This indicates no universal winner and a specimen-sensitive transition. All 16 spectral fits missed the 2% convergence tolerance. The next step is to improve the joint two-wave fit and investigate the Run 25 transition.