## Slide 1
Adaptive sinusoidal spectral matching
for out-of-plane masonry walls
Four Route 2 methods tested from the common Strategy F Run 21 state
Progress meeting, Hanze SAFEGo US-1 + US-2, 5 October 2026
Notes: This update focuses on the four Route 2 carrier and target combinations. Each sequence starts from the same Strategy F Run 21 save and carries the damage state forward through FR76 Runs 22–25.

## Slide 2
1
Four Route 2 methods
Two target rules crossed with two Wave B carrier periods
Method 1
B target: scale × Sd(Teff)
B carrier: Teff = 0.241 s
Wave A · T1 = 0.112 s
Wave B · carrier shown above
Method 2
B target: scale × Sd(Teff)
B carrier: record Tp = 0.260 s
Wave A · T1 = 0.112 s
Wave B · carrier shown above
Method 3
B target: (T*, d*) by intensity
B carrier: T* = 0.134 s
Wave A · T1 = 0.112 s
Wave B · carrier shown above
Method 4
B target: (T*, d*) by intensity
B carrier: record Tp = 0.260 s
Wave A · T1 = 0.112 s
Wave B · carrier shown above
Target = desired spectral displacement at an oscillator period. Carrier = input sine period. The fit adjusts wave velocities with carrier periods fixed; Methods 3–4 use precomputed targets.
Notes: Wave A is common to all four methods and targets scale × Sd(T1), where T1 is about 0.1119 s. Methods 1 and 2 use fixed target points at T1 and Teff, with Teff about 0.2414 s. Methods 3 and 4 use the precomputed capacity-proxy target d* and T* for each intensity. Method 1 carries Wave B at Teff; Method 2 uses the FR76 predominant period Tp = 0.260 s; Method 3 carries Wave B at T*; Method 4 uses Tp. The amplitude fit changes the two input velocity amplitudes while the carrier periods remain prescribed. The adaptive schedule is precomputed and independent of the preceding 3DEC response.

## Slide 3
2
Reading targets at fixed periods
T1 and Teff come from the wall idealisation; each run supplies a scaled record spectrum
Chart: Scaled spectral displacement Sd (mm)
Guides: T1 = 0.112 s (dark) · Teff = 0.241 s (terracotta)
Curves: HU12 (blue, 21 runs) · EC40 (green, 4 runs) · FR76 (terracotta, 4 runs)
Wave A target = scale × Sd(T1) · Method 1 Wave B target = scale × Sd(Teff)
Notes: All 25 lines are the 5%-damped displacement spectra for the run's ground-motion record multiplied by that run's protocol scale. T1 = 0.111887 s and Teff = 0.241382 s are the fixed periods from the wall's bilinear pushover idealisation and are reused for every run. For each run, the ordinate read at T1 sets the Wave A spectral-displacement target, and the ordinate read at Teff sets Method 1's Wave B target. The chart zooms the period axis to 0–0.35 s to make both fixed target periods legible. The lines are grouped by record; repeated curves have different protocol scales.

## Slide 4
3
Method 3 target for Run 22
A stable fixed point between the scaled FR76 spectrum and the cracked pushover backbone
d* = 1.00 × Sd,FR76(Tsec(d*))
Tsec(d) = 2π √[ meff / (Fcracked(d) / d) ]
TRIAL DISPLACEMENT
3.423 mm
Run 22 · FR76 × scale 1.00
PUSHOVER SECANT
12.360 kN
Fcracked at d* · ksec = F/d = 3.611 kN/mm
READ THE SPECTRUM
0.133704 s
Tsec → Sd,FR76 = 3.423 mm
meff = 1,635 kg → Tsec = 2π√(1,635 / 3.611×10⁶) = 0.133704 s
At that period, FR76 gives Sd = 3.423 mm. Demand equals the trial displacement, so this is d*.
The cracked backbone follows the precomputed target schedule after an earlier target crossed dy; Run 21's measured response is not used.
Notes: The value d*=3.423165 mm is read from Claude outputs/casm_step1_targets.csv for Run 22, FR76 at scale 1.00. The calculation uses the actual pushover force-displacement backbone and the 5%-damped FR76 spectrum. At d=3.423165 mm the cracked backbone gives F=12.360003 kN, hence F/d=3.610694 kN/mm. With m_eff=1635 kg, the secant-period calculation gives T*=0.133703694 s. Linear interpolation of the FR76 spectrum at that period gives Sd=3.423165 mm, so scale × Sd(Tsec(d)) equals d. The script numerically scans and interpolates the first stable crossing. The target schedule's cracked-backbone state is property-based damage memory: it switches after an earlier scheduled d* crossed dy; it does not read the measured Run 21 or Run 22 3DEC response. Method 3 uses this T* as its Wave B carrier before snapping to the 0.135 s time-grid period.

## Slide 5
4
Run 22 input velocity
Actual FR76 × 1.00 velocity tables imported into 3DEC · Wave A is common to all methods
Chart: Applied table velocity (m/s)
Method 3 · T_B = 0.135 s | 0 | 0.00227 | 0.0043562 | 0.0060894 | 0.0073293 | 0.0079754 | 0.0079754 | 0.0073293 | 0.0060894 | 0.0043562 | 0.00227 | 9.8675e-19 | -0.00227 | -0.0043562 | -0.0060894 | -0.0073293 | -0.0079754 | -0.0079754 | -0.0073293 | -0.0060894 | -0.0043562 | -0.00227 | -1.9735e-18 | 0.013019 | 0.025336 | 0.036287 | 0.045282 | 0.051835 | 0.055595 | 0.056357 | 0.054081 | 0.048889 | 0.041062 | 0.031021 | 0.019308 | 0.0065537 | -0.0065537 | -0.019308 | -0.031021 | -0.041062 | -0.048889 | -0.054081 | -0.056357 | -0.055595 | -0.051835 | -0.045282 | -0.036287 | -0.025336 | -0.013019 | -1.3827e-17
Wave A carrier = 0.110 s in every method. The fitting routine changes the Wave A/B velocity amplitudes; the selected carrier periods stay fixed.
Notes: Each series is read from the corresponding Run22_FR76_s1p00_*_vel.txt table saved in route2_four_methods and imported by the 3DEC Itasca Python script. These are the applied boundary/table velocities at the native 0.005 s sample interval, not wall response velocities. The common Wave A carrier is 0.110 s on the input grid. Wave B grid periods are 0.240 s, 0.260 s, 0.135 s, and 0.260 s for Methods 1–4. The carrier periods are set by each method; the joint spectral fit adjusts the component velocities.

## Slide 6
5
Peak response and spectral calibration
Runs 22–24 compare with US-1 Test 9; Run 25 has no matching specimen test
17.1%
Method 2 mean OOP error
9.3%
Method 1 mean base-shear peak error
All 16 spectral fits missed the 2% convergence tolerance. Treat these response rankings as provisional.
Notes: Metrics use the three experimental comparisons available for US-1 Test 9, Runs 22–24. Method 2 has the lowest mean absolute percentage error in peak relative OOP displacement at 17.1%. Method 1 has the lowest mean absolute percentage error in peak base shear at 9.3%. Run 25 is shown for the model sequence only because no US-1 Test 9 experiment exists for that run. The four methods used the common Strategy F Run 21 starting state. All 16 signal fits report fit_converged=False at the 2% tolerance, so the method ranking is preliminary.

## Slide 7
6
Peak-response comparison: Method 2 highlighted
Methods 1, 3 and 4 are muted; the experimental series remains visible
Method 2 has the lowest mean peak OOP error (17.1%); Method 1 still has the lowest base-shear error (9.3%).
All 16 spectral fits missed the 2% convergence tolerance; treat these rankings as provisional.
Notes: This is a visual focus transition from the preceding all-method comparison. Methods 1, 3 and 4 use one pale grey with partial transparency; Method 2 retains its orange emphasis, and the US-1 experiment remains black. The underlying data are unchanged. Method 2 has the lowest mean absolute peak relative OOP displacement error at 17.1%, while Method 1 has the lowest mean absolute peak base-shear error at 9.3%. All 16 spectral fits missed the 2% convergence tolerance, so these rankings remain preliminary.

## Slide 8
7
Two base-shear measures
cstav is a model support reaction; the test reports an inertia-derived estimate
DIRECT 3DEC OUTPUT
cstav
V_cstav(t) = sign × [cstav(t) − cstav(0)]
What it measures
The net reaction from the model’s base and joist supports, read directly from the 3DEC history.
Kept as a grey reference trace. It is not the quantity reported by the experimental processing formula.
TEST-COMPATIBLE INERTIA ESTIMATE
V_eq = sign × (λ / 1000) Σ m_j a_j,abs
kN · sign aligned and each run zeroed at its start
Acc 17 · z = 2.06 m
m17 = 404.13 kg
Acc 16 · z = 1.26 m
m16 = 320.66 kg
Acc 15 · z = 0.60 m
m15 = 408.52 kg
3DEC MODEL
Differentiate absolute sensor velocities; resample at 0.5 ms and low-pass at 50 Hz.
EXPERIMENT
Use table acceleration plus the wall accelerometers to reconstruct absolute acceleration.
LIKE-FOR-LIKE COMPARISON
The same Σm·a definition is used for the experimental data and reconstructed from the model’s sensor histories. Base-shear errors on the next slides use this estimate; cstav stays as context.
Mass basis: ρ = 1,619 kg/m³ gives the tributary masses above. λ = 2.317348 reproduces the factor in the processed tests and is applied to both sides; its origin is not confirmed.
Loops use relative OOP displacement at z = 2.06 m on the horizontal axis.
Notes: cstav is the direct model support reaction from the base and joist supports; the existing source plots it as a grey context trace. The experimental base shear is derived from accelerometer inertia (Moshfeghi et al. 2024, Eq. 2), not cstav. It uses the three sensor-point absolute accelerations at z=0.60, 1.26, and 2.06 m, weighted by tributary masses 408.52, 320.66, and 404.13 kg. The model side reconstructs those absolute accelerations by differentiating absolute out-of-plane velocities, resampling at 0.5 ms, and applying a 50 Hz low-pass filter. The processed test formula combines table acceleration and wall accelerometer channels to get absolute acceleration. The factor lambda=2.317348 is applied to both sides to reproduce the factor embedded in the processed tests; its origin is unknown and remains a question. Curves are start-zeroed, sign-aligned, and plotted against relative OOP displacement at 2.06 m. The reported model-to-test peak base-shear errors use the experimental-derived sum(m*a) quantity, not cstav.

## Slide 9
8
Base shear versus OOP displacement: Method 1
Like-for-like loops from baseshear_exp_from_model.py
US-1 Test 9 is the primary experimental comparator. US-2 Test 12 and the support series remain visible in the source figure.
Base-shear mass basis
Tributary masses use ρ = 1,619 kg/m³; the ×2.317348 test factor is applied to both model and experiment.
US-1 mean base-shear peak error
9.3%
Notes: Method 1 uses the per-method plot generated from the project copy of Claude outputs/baseshear_exp_from_model.py. The script sums tributary masses at sensors 15–17 using ρ = 1,619 kg/m³ and applies MASS_SCALE = 2.317348 to both the model and experimental sides. The source figure retains both US-1 Test 9 and US-2 Test 12, plus the support reaction traces. The displayed mean base-shear peak error is specific to US-1 Test 9, Runs 22–24; a separate slide scores US-2 over Runs 22–25.

## Slide 10
9
Base shear versus OOP displacement: Method 2
Like-for-like loops from baseshear_exp_from_model.py
US-1 Test 9 is the primary experimental comparator. US-2 Test 12 and the support series remain visible in the source figure.
Base-shear mass basis
Tributary masses use ρ = 1,619 kg/m³; the ×2.317348 test factor is applied to both model and experiment.
US-1 mean base-shear peak error
13.3%
Notes: Method 2 uses the per-method plot generated from the project copy of Claude outputs/baseshear_exp_from_model.py. The script sums tributary masses at sensors 15–17 using ρ = 1,619 kg/m³ and applies MASS_SCALE = 2.317348 to both the model and experimental sides. The source figure retains both US-1 Test 9 and US-2 Test 12, plus the support reaction traces. The displayed mean base-shear peak error is specific to US-1 Test 9, Runs 22–24; a separate slide scores US-2 over Runs 22–25.

## Slide 11
10
Base shear versus OOP displacement: Method 3
Like-for-like loops from baseshear_exp_from_model.py
US-1 Test 9 is the primary experimental comparator. US-2 Test 12 and the support series remain visible in the source figure.
Base-shear mass basis
Tributary masses use ρ = 1,619 kg/m³; the ×2.317348 test factor is applied to both model and experiment.
US-1 mean base-shear peak error
14.7%
Notes: Method 3 uses the per-method plot generated from the project copy of Claude outputs/baseshear_exp_from_model.py. The script sums tributary masses at sensors 15–17 using ρ = 1,619 kg/m³ and applies MASS_SCALE = 2.317348 to both the model and experimental sides. The source figure retains both US-1 Test 9 and US-2 Test 12, plus the support reaction traces. The displayed mean base-shear peak error is specific to US-1 Test 9, Runs 22–24; a separate slide scores US-2 over Runs 22–25.

## Slide 12
11
Base shear versus OOP displacement: Method 4
Like-for-like loops from baseshear_exp_from_model.py
US-1 Test 9 is the primary experimental comparator. US-2 Test 12 and the support series remain visible in the source figure.
Base-shear mass basis
Tributary masses use ρ = 1,619 kg/m³; the ×2.317348 test factor is applied to both model and experiment.
US-1 mean base-shear peak error
17.1%
Notes: Method 4 uses the per-method plot generated from the project copy of Claude outputs/baseshear_exp_from_model.py. The script sums tributary masses at sensors 15–17 using ρ = 1,619 kg/m³ and applies MASS_SCALE = 2.317348 to both the model and experimental sides. The source figure retains both US-1 Test 9 and US-2 Test 12, plus the support reaction traces. The displayed mean base-shear peak error is specific to US-1 Test 9, Runs 22–24; a separate slide scores US-2 over Runs 22–25.

## Slide 13
12
US-2 is a separate benchmark
The Test 12 displacement path stays low through Run 24, then rises sharply at Run 25
Chart: Peak relative OOP displacement (mm)
| 22 | 23 | 24 | 25
Method 1 | 3.3132 | 24.0228 | 31.823 | 34.1371
Method 2 | 2.4738 | 12.1028 | 32.7545 | 41.014
Method 3 | 3.5841 | 5.8417 | 7.4077 | 9.9228
Method 4 | 2.25 | 5.3268 | 28.2426 | 36.3054
US-1 Test 9 | 3.6473 | 13.1536 | 29.4828
US-2 Test 12 | 2.3847 | 5.2645 | 7.5808 | 31.1419
Chart: Peak experiment-equivalent base shear (kN)
| 22 | 23 | 24 | 25
Method 1 | 17.7439 | 29.0586 | 31.8247 | 36.527
Method 2 | 18.4502 | 26.5624 | 38.0256 | 32.525
Method 3 | 21.3379 | 20.0858 | 25.5861 | 22.9949
Method 4 | 20.9988 | 21.8173 | 37.98 | 39.8456
US-1 Test 9 | 20.3266 | 27.041 | 29.5
US-2 Test 12 | 21.1914 | 27.8652 | 29.9902 | 38.0722
RUN 24
3.9×
US-1: 29.48 mm · US-2: 7.58 mm
US-2 RUN 25
31.14 mm
Large excursion; US-1 has no Run 25 test.
US-2 MEAN ABSOLUTE ERROR
OOP: M3 32.9% · Shear: M1 7.7%
M3 tracks through Run 24, then misses Run 25.
The model sequences start from the US-1 Strategy F Run 21 state; Test 12 is an independent specimen check. US-1 and US-2 are not pooled.
Notes: US-2 Test 12 workbooks were post-processed with the same start-zero peak definition used for US-1: U_avg converted from metres to millimetres, and processed base_shear_kN zeroed at each run start. The four method response peaks are compared with the four Test 12 observations, Runs 22–25; these sequences all start from the common US-1 Strategy F Run 21 model state. US-2 peaks are 2.385, 5.264, 7.581, and 31.142 mm displacement, with 21.191, 27.865, 29.990, and 38.072 kN base shear. US-2 Run 24 displacement is 7.58 mm against US-1's 29.48 mm, while Test 12 then reaches 31.14 mm at Run 25. Mean absolute percentage errors over Runs 22–25: Method 3 is lowest for displacement (32.9%) and Method 1 is lowest for base shear (7.7%). The 32.9% displacement error is still substantial: Method 3 matches US-2 Runs 23–24 closely, but its Run 25 model displacement is only 9.92 mm and it misses the large excursion. Methods 1, 2, and 4 instead produce large model excursions by Run 24. These results show different timing of the transition and specimen-specific sensitivity, not a universal winner.

## Slide 14
13
Experimental tiltmeter residuals
Settled sensor readings for US-1 and US-2; only US-2 has a Run 25 observation
Chart: Settled residual tilt Y (degrees)
| 21 | 22 | 23 | 24
US-1 Test 9 | 2.768 | 2.533 | 2.417 | 6.034
US-2 Test 12 | 1.223 | 1.0225 | 0.385 | 0.944 | 2.288
US-1 +3.266°
Run 24 change from its Run 21 reading
US-2 +1.065°
Run 25 change; settled reading 2.288°
Within-shaking peaks clip near ±25.75°; this plot uses settled residual readings only.
These are instrument readings. The model's local-chord angle is excluded from this comparison.
Notes: US-1 and US-2 tiltmeter residuals are recomputed with the same rule from EXP_DATA/US1_Tilt_values.csv and EXP_DATA/US2_Tilt_values.csv: use accelerometer swing to identify shaking events, then take the settled median after each event relative to the median of the first five samples. US-1 Runs 21–24 = 2.768, 2.533, 2.417, and 6.034 degrees; Run 24 is +3.266 degrees relative to Run 21. US-2 Runs 21–25 = 1.223, 1.0225, 0.385, 0.944, and 2.288 degrees; Run 25 is +1.065 degrees relative to Run 21. The within-shaking inclinometer peaks clip near ±25.75 degrees, so settled readings are shown. This slide compares the two experimental instruments only; it does not plot the model's local-chord tilt proxy.

## Slide 15
14
What these runs support
The method ranking depends on response metric and specimen
17.1%
Method 2
Lowest US-1 mean OOP
displacement error
9.3%
Method 1
Lowest US-1 mean base-shear
peak error
16 / 16
All methods
Spectral fits outside
2% tolerance
US-2 adds a different result: Method 3 has the lowest mean displacement error, while Method 1 leads on base shear.
Method 3 still misses the sharp US-2 Run 25 displacement jump; refine the fit and investigate this transition.
US-1 is scored over Runs 22–24; US-2 over Runs 22–25. Tests stay separate; models start from US-1 Strategy F Run 21.
Notes: The headline US-1 metrics compare Runs 22–24: Method 2 has the lowest mean absolute OOP error at 17.1%, and Method 1 the lowest mean absolute base-shear peak error at 9.3%. The separate US-2 score over Runs 22–25 gives Method 3 the lowest OOP MAPE at 32.9% and Method 1 the lowest base-shear MAPE at 7.7%. Method 3 predicts only 9.92 mm at US-2 Run 25 versus the measured 31.14 mm. This indicates no universal winner and a specimen-sensitive transition. All 16 spectral fits missed the 2% convergence tolerance. The next step is to improve the joint two-wave fit and investigate the Run 25 transition.